## Slide 2: Cellular
International Mobile Equipment Identity
  Worldwide hardware identifier
  GSM and UTMS networks
  Potential for spoofing
International Mobile Subscriber Identity
  Worldwide unique subscriber identifier
  GSM and UTMS networks
  Stored in Subscriber Identity Modules(SIM)
Notes: 15- or 17-digit code that uniquely identifies mobile phone sets.
The IMEI code can enable a GSM (Global System for Mobile communication) or UMTS (Universal Mobile Telecommunications Service) network to prevent a misplaced or stolen phone from initiating calls.

## Slide 3: Wi-Fi
IEEE 802.11* standard
  .11a – Wi-Fi 2 ( 54 Mbps, 5 GHz)
  .11b – Wi-Fi 1 ( 11 Mbps, 2.4 GHz)
  .11g – Wi-Fi 3 ( 54 Mbps, 2.4 GHz)
  .11n – Wi-Fi 4 ( 2.4/5 GHz, 600 Mbps)
  .11ac – Wi-Fi 5 (5 GHz, 3.6 Gbps)
  .11ax – Wi-Fi 6 (2.4/5/6 GHz 14 Gbps)
Notes: WiFi 1 = 1999
WiFi 2 = 1999
WiFi 3 = 2003
WiFi 4 = 2009
WiFi 5 = 2014
WiFi 6 = 2019

## Slide 4: Near Field Communication (NFC)
Short-range communication
  (10cm/4 inches)
13.56 MHz base frequency
Simple setup
File/data transfer
Notes: Client presents the list of supported cipher suite

## Slide 5: Infrared
Short-range communication
  1 meter/3.28 ft
Sensitive LoS communication
IrDA
16 Mbps
Notes: Client presents the list of supported cipher suite

## Slide 6: Bluetooth
Data transfer
Fixed and mobile devices
Discovery and pairing
2.4 GHz spectrum
Notes: Enhanced Data Rate

## Slide 7: Bluetooth Standards
1.0,1.2(legacy) = 732 Kbps
2.0, 2.1 (+EDR) = 3 Mbps
3.0 (+HS) = 24 Mbps
4.0/4.2 (+BLE) = 3 Mbps
Notes: Enhanced Data Rate
High speed
Bluetooth low energy

## Slide 8: Universal Serial Bus
Point-to-point communications
Data transfer
Standards
  1.1 (Full speed) = 12 Mbps
  2.0 (High speed) = 480 Mbps
  3.2 Gen 1 (SuperSpeed) = 5 Gbps
  3.2 Gen 2 (SuperSpeed+) = 10 Mbps
  3.2 Gen 2x2 (SuperSpeed 10Gbps) = 20 Gbps
  USB 4 (USB4 Gen3x2 40 Gbps) = 40 Gbps
Notes: Client presents the list of supported cipher suite

## Slide 9: Global Positioning System
Components
  Space segment
  Control segment
  User segment
Global Navigation Satellite Systems
  GPS (US)
  GLONASS (Russia)
  Galileo (EU)
  BeiDou (China)
Notes: Space segment = 24 operational satellites, 3 stand-by (27 total), transmitting one-way signals
Control segment = worldwide monitoring system, control stations (command maneuvers)
User segment = GPS receiver

## Slide 10: Radio Frequency Identifier
Electromagnetic fields
Identify and track tags
Tags attached to objects
Tag types
  Passive tags = powered by RFID reader
  Active tags = battery powered
Notes: Client presents the list of supported cipher suite

## Slide 11: Security Concerns
Eavesdropping
Data leaks
Replay attacks
Spoofing attacks
Unauthorized use
Notes: Bluesnarfing = data theft
Bluejacking = unauthorized use
PII, proprietary information