## Slide 2: Layer 2 Attacks
ARP Poisoning
MAC Cloning
MAC Flooding

## Slide 3: Layer 2 and OSI Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Access to network resources
Formatting to standard format
Opening, closing, maintaining communication
Sequencing, segmentation, host-to-host communication
Addressing and routing
LAN communications, forwarding, media access
Electrical communications, media

## Slide 4: ARP Process
Data Link
Network
10.10.10.10
01-02-03-AA-BB-CC
ARP
Local Broadcast
Who has 10.10.10.10?
Tell 10.10.10.10 is at 01-02-03-AA-BB-CC
ARP Cache
Notes: Show ARP Table

## Slide 5: Layer 2 Attacks – ARP Poisoning
Source computer
ARP Cache
Local Broadcast
Who has 10.10.10.10?
10.10.10.10 is at attacker’s MAC
Notes: Show ARP Table
Show Wireshark with ping to bogus IP
Show the ARP process trying
Then show legit/complete process

## Slide 6: MAC Address Cloning
01-23-78-AB-CD-EF
Computer A
00-A3-D2-CC-12-EE
Computer B
Notes: Show ARP cache
Show Wireshark with ping to bogus IP
Show the ARP process trying
Then show legit/complete process

## Slide 7: MAC Address Cloning
01-23-78-AB-CD-EF
Computer A
00-A3-D2-CC-12-EE
Computer B
macchanger
01-23-78-AB-CD-EF
Notes: Show ARP cache
Show Wireshark with ping to bogus IP
Show the ARP process trying
Then show legit/complete process

## Slide 8: Layer 2 Attacks - MAC Flooding
MAC Address | Port #
01-00-03-AA-BB-CC | 10
02-03-04-DD-EE-FF | 22
11-22-33-AB-CD-EF | 43
-- | --
-- | --

## Slide 9: MAC Flooding
MAC Address | Port #
01-00-03-AA-BB-CC | 10
02-03-04-DD-EE-FF | 22
11-22-33-AB-CD-EF | 43
00-11-33-DE-F3-E2 | 05
00-12-33-00-12-AE | 13
00-11-33…
00-12-33…
01-12-33…
01-12-33…
Notes: Show MAC address

## Slide 10: MAC Flooding
Fail-open
Flood all ports with broadcast traffic
Sniffing
Store/use all data