## Slide 2: Extensible Authentication Protocol
Framework for authentication
Used in wireless networks
Expands upon PPP authentication
Supports multiple authentication types
Notes: Authentication types are called EAP methods

## Slide 3: EAP Methods
EAP-FAST
EAP-TLS
EAP-TTLS
Notes: EAP-FAST, also known as Flexible Authentication via Secure Tunneling, is an EAP (Extensible Authentication Protocol) developed by Cisco. It is used in wireless networks and point-to-point connections to perform session authentication.
EAP-TLS, which includes support for certificate-based mutual authentication, and smartcards

## Slide 4: 802.1X
Port-based authentication
Components
  Supplicant
  Authenticator
  Authenticator Server
Notes: Do not confuse with 802.11x

## Slide 5: 802.1X
Supplicant
Authenticator
Authentication Server
(Wireless Client)
(802.1X compliant AP/WLC)
(RADIUS Server)
WLAN controller