## Slide 2: Authentication Protocols
Communication Protocol
Secure credential transfer
I am…..
Prove it…
Username/Password
798i6p;ufr;8l75ers654$#@

## Slide 3: Point-to-point Protocol
PPP
  Components
    Link Control Protocol
    Authentication Protocol
    Network Control Protocol

## Slide 4: PPP Components
Link Control Protocol
  Establishes, configures, maintains connection
  Handles authentication
Authentication Protocol
  Determines the authentication protocol
  PAP, CHAP
Network Control Protocol
  Determines how to handle L3 protocols

## Slide 5: Password Authentication Protocol
Bob/P@ssw0rd123
Authentication Request
Authentication-ack
Authentication-nack

## Slide 6: Challenge Handshake Authentication Protocol
Bob’s password encrypts challenge
Challenge (random bits)
Authentication Confirmed
Authentication Request
Bob’s password decrypts challenge
Bob’s password
Bob’s password

## Slide 7: CHAP Variants
CHAP
  Non-Windows environments
MS-CHAP
  Microsoft’s CHAP implementation
  Weak
MS-CHAPv2
  Mutual authentication
  Stronger cryptographic keys

## Slide 8: Extensible Authentication Protocol
Framework for authentication
Used in wireless networks
Expands upon PPP authentication
Supports multiple authentication types
Notes: Authentication types are called EAP methods

## Slide 9: EAP Methods
EAP-FAST
EAP-TLS
EAP-TTLS
Notes: EAP-FAST, also known as Flexible Authentication via Secure Tunneling, is an EAP (Extensible Authentication Protocol) developed by Cisco. It is used in wireless networks and point-to-point connections to perform session authentication.
EAP-TLS, which includes support for certificate-based mutual authentication, and smartcards

## Slide 10: 802.1X
Port-based authentication
Components
  Supplicant
  Authenticator
  Authenticator Server
Notes: Do not confuse with 802.11x

## Slide 11: 802.1X
Supplicant
Authenticator
Authentication Server
(Wireless Client)
(802.1X compliant AP/WLC)
(RADIUS Server)
WLAN controller

## Slide 12: Remote Authentication Dial-in User Service
Open standard
Uses UDP ports
Centralizes
  Authentication
  Authorization
  Accounting
Notes: 1645

## Slide 13: Authentication Protocols
Terminal Access Controller Access Control System (TACACS)
  Cisco Proprietary
  Separates the AAA roles
  Used TCP and encryption
Notes: Do not confuse with 802.11x

## Slide 14: Authentication Protocols
RADIUS | TACACS+
Authentication, Authorization and Accounting | Separates Authentication and Authorization
Lack of multiprotocol support | Multiprotocol support
Uses UDP (password only encryption) | Uses TCP (Full encryption)
Open standard | Proprietary
Notes: TACACS+ This allows separate authentication solutions that can still use TACACS+ for authorization and accounting. For example, with TACACS+, it is possible to use Kerberos authentication and TACACS+ authorization and accounting.
- AppleTalk Remote Access (ARA) protocol
- NetBIOS Frame Protocol Control protocol
- Novell Asynchronous Services Interface (NASI)
- X.25 PAD connection

## Slide 15: Authentication Protocols
Access Client
RADIUS Client
RADIUS Server
802.1X compliant AP
VPN Server
Dial-up Server
Access request
RADIUS message
RADIUS challenge
RADIUS challenge
Access granted
Access denied

## Slide 16: Authentication Protocols
Kerberos
  Developed by MIT
  Open-source
  Time-sensitive authentication
  Default for MS Active Directory
Notes: Do not confuse with 802.11x

## Slide 17: Authentication Protocols
Kerberos
  Components
    Authentication Server
    Key distribution center
    Ticket-granting ticket
    Ticket-granting service
Notes: Do not confuse with 802.11x

## Slide 18: Authentication Protocols
TGT Stored
Authentication Request
Authentication verified/Encrypted TGT
Kerberos Server
TGT is sent to TGS with name of resource
Session key issued
Resource Server
Session Key